Intructions on how to convert your Fortec STAR Lifetime Ultra to a Pansat 2700 CLONE.

First, here's a list of tools that you need: 

- RS 232 female-female STRAIGHT CABLE 
- Fortec STAR Lifetime Ultra remote control

Instructions/Procedure:

- Please turn OFF your receiver and disconnect it from the satellite & the TV cable

- Connect your receiver to your computer using RS 232 female-female STRAIGHT CABLE serial cable

- Turn ON your receiver and wait 20 seconds

- Open the FortecSTARSTB loader and select the boot file (b75_m.bin)

- On the loader's screen, under the Type options, please select Boot

- Now, please select the correct computer port (COM 1 or COM 2)

- Make sure your receiver is still ON and connected to your computer

- Now, on the loader's screen, please click Download

- Now, wait for it to complete

- After it's completed, you'll see B 7 5 flashing on your receiver's front panel/screen

- Now, please close the loader's window and leave your receiver turned ON

- Now, it's time to load the actual flash bin file into your receiver

- Please re-open the FortecSTARSTB loader and select the flash bin file (jvvh_208_1.bin)

- On the loader's screen, under the Type options, please select Flash

- Now, please select the correct computer port (COM 1 or COM 2)

- Make sure your receiver is still ON and connected to your computer

- Now, on the loader's screen, please click Download

- Now, wait for it to complete

- After it's completed, you'll see B 7 5 flashing on your receiver's front panel/screen

- That flashing B 7 5 will stop and freeze on number 5 for 30 seconds

- After 30 seconds or so, your receiver will automatically boot (It'll turn ON automatically, after 30 seconds)

- Now, please turn your receiver OFF and disconnect it from your computer

- Finally, please connect the satellite and the TV cable to your receiver

- That's It, you're done! Now, you have a Pansat 2700 Clone receiver

Note: After you finish with the above steps, you have to re-scan your satellite(s). After you're done with that, you have to enter the latest keys (Dishnetwork or BellExpressVu). Here's what you need to do after you re-scan your satellite(s):

- Go to MENU

- Then, go to Parental Control

- Then, go to Second Pin and enter 0000

- Then, go to Set Default Key

- Then, go to Nagravision 2 to enter the latest Dishnetwork or BellExpressVu keys

After you enter and store the latest keys, please EXIT the menu and start watching TV!