Loading SonicView with Null Serial Cable

1. Download SonicView Downloader v0201 and Current Working Bin Sonicview SV4000

2. Place all files in the same folder as loader is located.

3. With SV-4000 turned off at the back, connect null modem cable from FTA box to PC/laptop.

4. Start loader program, Click STB -> Connect Config for Com 1 or any com port # that you PC is preference.

5. Click STB -> Download file (PC->STB) directing the downloader to the file you are wanting to load.

6. Window appears entitled Data Transfer -> Turn VS 4000 on from the rear power button and do not touch it until transfer is complete and SV4000 reboots.

7. Turn off SV-4000 at rear, disconnect null modem cable


Note: If you have difficult, experiment the receiver lock up, get SonicView 4000 Factory Bin then following the procedures from the above.

**--   **--   **--   **--   **--   **--   **--   **--   **--   **--   **--   **--   **--   **--

First of all I would like to thank Mr.Parmy from Viewsatonline for providing me this awsome receiver to test and review . This report is base on my own testing and opinion.
The package come with 1 RCU , 1 package of battery, 1 set of RCA cable and 1 NULL cross modem cable.
The remote is a little diffrent than the SV-1000 that I had. They eliminate the 2 extra button next to the left and right of 0 button( anyway they are useless in SV 1000)
The back pannel : TV out is on top next to LNB in connector port ( SV 1000 TV out port is next to LOOP out port)

I connected it all up and turn the back power switch to ON switch and the clock displayed 12:00 after a good to 2 seconds offlashing lines ( I think is normal), Then I pushed the STB button on the remote control button on the remote "Boot".. "Boot"... "Lang".. and the language screen appeared on the tv screen and I selected "English". Then the Info screen appeared on the tv screen saying "No Channel".

I went to menu - receiver info and at this point is has a factory bin on it and Version information displays Bootloader version 01.00 and Main Software Version 00.99

Next I downloaded and unzipped the Autoroll bin to the USB ( You have to purchase this USB ,not come with the package)flash drive (v115) and stuck the USB flash drive into the USB slot which is located on the front, behind the accessory door on the right hand side of the receiver. 

Once the USB flash drive was inserted into the USB slot, I pressed Menu, Installation and went to USB Mass Storage and clicked OK on the remote. It brings up a USB Mass Storage folder and you can arrow to the file you want to select (I also have the ULTRA file stored on this same USB ) and press the RED (Not the power RED ) button on the remote to Update Software.

The actual bin took about 3 seconds to load.. Pretty fast compaered to tranfer file use cable and a bit faster then ULTRA. At this point the TV screen it said "Software Downloading" and then "DO NOT POWER OFF!!" and says "Flash Updating" then Flash Updating turns to "Reboot" and then on the receiver display say's "Save".."Good"..----.."Save".."Boot".."Save".."Boot" and then the on the display is "0000". This procedure took about closed to 1 minute

And if you you do not have a USB flash drive then you can also use the supplied Null Modem cable and flash through the serial port on your computer with the same loader that the SV-1000 uses, loader v0201.

Before setting up satellites it's a good idea to set up the menu options first.

1: Time. Make sure your time and date are set correctly. This is important for properly populating the Electronic Program Guide.
I didn't even have to up dated my time. If you change the date and time manually don't forget to put it back to AUTO before you exit or you will have problems with the EPG.

2: User Options. Turn everything ON except Auto Dolby Select and Closed caption and select your state and locals .I selected California and Sanfrancisco ( since my city is not on the list I choose the close by city /local in the provided list ) 
I have a DP 500 -twin LNB + a DP-34 switch to 4 receivers aiming at 110W and 119W
ANTENNA SETTING:
LNB type = OCS-DP.LNB freqc = 11250with 22KHz = OFF.DISEqc with 119W on port 1 and 110W on port 2
SCAN:
Press Menu on the remote and go to Installation ENTER DEFAULT PIN CODE -0000-and set up your satellites and when you set each one up making sure your LNB Type and Switch Settings are correct and the POPED UP Sat Info box will showed up in the top right hand corner of the screen indicating which satellite your working with. Make sure that banned will match with that SAT you try to setting up.If that number in the blue box does not match the satellite your working with, then your switch settings are incorrect or your dish isn't in the proper alignment. Once all of your settings are correct, Press the Red Button on the remote to scan just that satellite. Red button scanning prevents duplicates in your channel list which can cause trouble with the EPG.
Sat scanning is fast in just under 2 minutes for each SAT . I also try to use the blind scan -GREEN- button to scan ( it tooks a good 7 minutes to blind scan ) ,have the same amount of channel coming in as use RED button to scan . YELLOW button -scan all- scan as fast as RED
After successed with scanned and saved I go to channel200 on ECHOSTAR 7n and way for Keys to roll , in about closed to 3 minutes I had have picture 
EPG:
I am most impressed with this. On DN full EPG on ch 239 with power ON was almost instant for a 2 days as I sit on that channel for 3-4 minutes 7 days EPG has populated . I am very amazing about EPG populates so fast !!

Other nice Features include:

Browse EPG by Catagory
Guide Search
Parental Control (Ratings limits, Lock or hide porn )
Event Timer
Manual key entry if necessary
Fast Autoroll
Channel Sorting by SID
Universal Remote Control to control your SV-4000/TV/VCR/DVD player
7 Day EPG on Dn and 44 hours on northern sat)
Picture is abit clearer and sharper then SV1000
Picture Quality is incredible with Component out or S-Video 
After played with it for a while I had run into a small problem with rebooting when I scrolled the EPG by holding down the UP or DOWN button, The receiver FREEZED I have to hardboot ( turn back power switch to OFF and back to ON )
RCUs sensor eye is still need to realigned in order to work 
I find this unit is big step up from its older brother the SV-1000 and the SV-4000 should be good addition to anyone looking for the latest features or if your PC does not have the 9-PIN connector and the best picture quality on the market. I am truly impressed by the performed of this receiver via USB loading port(very fast) picture quality and how the EPG populates virtually instantly, even after a reboot. It is a very impressive unit.

__________________

These suggestion only base on my testing. Take them as your own risk

NO HARD FEELING