How to Update your Viewsat Xtreme FTA Receiver

Updated Aug 14, 2006

You must Download (or have already downloaded previously) all files listed below. Click on the BLUE download button on the website and select SAVE. *** DO NOT TRY TO OPEN or RUN these files at this time.

Loader2.exe     <--- this is the program used to update your FTA

Zmodem32.dll    <--- this file is used by the Loader2.exe program.

Must be in the same folder with Loader2.exe

UEN2_vsX_Aug14.pgm     <--- All channels working, WITH AUTO-ROLL.

(Always use only the newest flash posted on the website as these instructions may be slightly out-of-date)

Programming (Flashing) your Viewsat Xtreme

1.	PLUG in ViewSat; turn rear POWER switch “OFF”. Connect ViewSat to computer Com1 Port via Null Modem cable

2.	Open the program "Loader2. Click on tool, click on configuration and select the comm. port, Click "Open Files", select “UEN2_vsX_Aug14.pgm” to write to the ViewSat.

3.	 Click on PC-->STB button, then go press the Power “ON” switch on your ViewSat rear panel. (You should see the File loading properly)

4.	WAIT! DO NOT TOUCH VIEWSAT!!! It will load the file. After file transfer is  complete, the front panel will display “INST” for 15 seconds while it installs the software; “End” is displayed for about the next 10 seconds; then “ 00.00 “ 

. . . . . Front Panel goes to “0000”; you may switch power “OFF” and hook up to your TV

5.	 Connect your wire from the Satellite Dish to the LNB input on the back of your receiver.

6.	 Plug ViewSat into the wall socket and turn rear power switch “ON” .

Connect your receiver back to your TV....do the steps below after connected

Auto-roll must be turned ON !!!

Press MENU (you may be asked for a password - if so use 0  0  0  0 )

Select OPTIONS

AUTO-ROLL = ON !!!

Press EXIT to return to TV and all channels should now be working again!

Change to your favorite channel, such as USA or PPV channel.

Auto-roll will take a few minutes to roll the keys.During this time you will not see any indication that keys are rolling.

TV will just come in all of a sudden. (as usual in the past)

We're back !!!!!!!

Will+Fern

U-Neek Electronics